## Slide 1
New MCA 160 kW
WALL-HUNG GAS CONDENSING BOILERS

## Slide 2: Objectives of the offer
To extend the MCA Pro range with a 160-kW model:
  Which is very compact
  And can be integrated in a cascade system with MCA PRO 45-115
  Max output in cascade up to 1160 kW
To integrate the new electronic platform

## Slide 3: Innovens Pro MCA 160
The strong points :
  From 114 to 160 kW (50/30 °C)
  From 107 to 153 kW(80/60 ° C)
  Modulation from 20 to 100%
  ∆t flow/return until 40°C
  Flap cascade integrated
  Sound level 55 dB (A)
  New control platform
  Easy installation and easy maintenance
  Full accessibility by the front of the boiler
  Internal lighting

## Slide 4: The global PACTA Project
1 WH version of 160kW
4 FSB executions from 160 to 300 kW

## Slide 5: Heat exchanger
Monobloc Aluminium-Silicium (AlSi )
With a sight glass
Very good ratio Output/Volume

## Slide 6: Heat exchanger - Inspection
Cleaning knife (560 mm , like C330)

## Slide 7: Innovens Pro MCA 160kW
MCA 160
67% soit 102KW
  ∆t flow/return until 40°C
  DHW outputs can be 67% of boiler output

## Slide 8: Dimensions and weight
Compact dimensions
Flue gas Ø 150 mm
Air intake Ø 150 mm
Siphon Ø 25 mm
Flow 1¼ inch
Return 1¼ inch
Gas 1 inch
Weight 123kg
(installation with an assistance recommended by De Dietrich)
600
602
305
143
80
110 Gas
240 Outlet
300 Condensats
425 Return
226
Flue gas
air
1045

## Slide 9: Two control panel executions
MK2
Application:
Auxiliary boiler in a cascade system
Boiler managed in 0/10V
SCB 01 in std
Application:
3 heating circuits + DHW
Master boiler in a cascade system
SSCB10 in Std
Diematic Evolution
Inicontrol 2

## Slide 10: Innovens Pro MCA 160
COMMUNICATION
Master boiler
Platine AD 286/287
OpenTherm (OT) entree on boiler PCB
Current MCA PRO range
Câble BUS
Only as slave
MCA PRO avec IniControl 2 et SCB-01

## Slide 11: Innovens Pro MCA 160
COMMUNICATION BUS CAN to BMS systems
MCA PRO avec IniControl 2 et SCB-01
Gateways in developpment for:
- Backnet
- KNX
- Modbus

## Slide 12: Delivery / Crating

## Slide 13: Unpacking
Online instruction

## Slide 14: Documentation
Pre installing - Documentation
Manual Innovens pro MCA 160
MK2 MK3 control
Drilling template
Water quality
Sticker gas setting

## Slide 15: Installation box
Siphon
Hose
Support
Connection cables
HMI (MK2 or MK3)
Connection box
Fixing materials
Cleaning tool

## Slide 16: Installing - Connection box
Easy waring

## Slide 17: Installing - Connections
Flue gas Ø 150 mm
Air inlet Ø 150 mm
Concentric Excentric
Ø 110/150mm (standard FR )
option

## Slide 18: Standard regulation with inicontrol2
SCB 01

## Slide 19: Options Regulation inicontrol2
SCB 02

## Slide 20: Standard regulation with Diematic Evolution
SCB 10

## Slide 21: Cascade kit
Cascade kit for MCA 160
compatible with the others « MCA 15,25,35,… » without insulation or…

## Slide 22: Cascade kit
With insulation

## Slide 23: Launching
- March 2017 with Diematic Evolution